## Slide 1
PSUT – AI & Datamining Courses
Dr. Rawan Ghenmat & Dr. Nailah Madi SESAME Synchrotron | Machine Failure Prediction Project
Mar 3, 2024
Mustafa Ali Alzubi
Datamining and AI | Proposed Project

## Slide 2
Introduction to SESAME Facility
Introduction to the problem
Available resources
Project idea
Similar work done
Datamining and AI |Topics

## Slide 3
Datamining and AI |What is SESAME?
SESAME: Synchrotron-light for Experimental Science and Applications in the Middle East
A 3rd Generation Light Source that has state-of-the-art infrastructure which designed to enable the scientific research in the region for designated users communities
Located in
Jordan
Our doors
are opened
To the rest
of the world
For scientific collaboration

## Slide 4
The first and only synchrotron in MENA
Members & observers countries are 25 -- CERN and EU.
The first and only synchrotron in the world that is powered by green enargy
Excellence centre in the ME
International, multicultural and non-profit organization
Datamining and AI | SESAME is Unique Research Centre

## Slide 5
Datamining and AI |How it works ??

## Slide 6
Datamining and AI |How it works??

## Slide 7
No | Beamline | Energy Range | Source Type | Status
BM02 | IR (Infrared) spectromicroscopy | 0.001-3 eV | Bending Magnet | Serving users
BM08 | XAFS/XRF (X-ray Absorption Fine Structure/X-ray Fluorescence) spectroscopy | 4.5-30 keV | Bending Magnet | 
ID09 | MS (Materials Science) | 5-25 keV | MPW | 
ID11 L | HESEB: Helmholtz-SESAME Beamline | 70-1800 eV | Undulator | Commissioned
ID10 | BEATS: Beamline for Tomography at SESAME | 8-50 keV | 3-Pole Wiggler | Installation
ID11 R | TXPES: Turkish X-ray Photoemission Spectroscopy | 70-1800 eV | Undulator | Design
 | MX Macromolecular Crystallography | 4 - 14 keV | In-Vacuum Undulator | Planned
 | SAXS (Small Angle X-ray Scattering) | 8 keV | In-Vacuum Undulator | 
Datamining and AI |Current and Future Beamlines

## Slide 8
Life science
Material Science
Chemical Science
Cultural heritage
Human remains
µ-tomography
Drugs design
New material
Agriculture
X-ray
Datamining and AI | Beamlines Applications

## Slide 9
Introduction to SESAME Facility
Introduction to the problem
Available resources
Project idea
Similar work done
Datamining and AI |Topics

## Slide 10
Datamining and AI | Problem Introduction

## Slide 11
Datamining and AI | Problem Introduction

## Slide 12
Datamining and AI | Why is it important to minimize failure time ??
BEST: BEame SatisFaction Report … We want to keep our scientist happy. Also we want to keep the machine in safe and good conditions

## Slide 13
Datamining and AI |How is it being managed currently ??
Machine
1K++ devices
EPICS Control System
Archiver
Elog
Operators have control and monitor terminals that they use to keep the machine running. If they can find problems before they happen, even just a few minutes before, it can help keep the machines running. But it's really hard to watch for every little thing that could go wrong. Maybe machine learning or deep learning can help with this?

## Slide 14
Introduction to SESAME Facility
Introduction to the problem
Available resources
Project idea
Similar work done
Datamining and AI |Topics

## Slide 15
Datamining and AI | Data sources | Archiver

## Slide 16
Datamining and AI | Data sources | Archiver

## Slide 17
Datamining and AI | Data sources | Archiver

## Slide 18
Datamining and AI | Data sources | Elog
Details

## Slide 19
Introduction to SESAME Facility
Introduction to the problem
Available resources
Project idea
Similar work done
Datamining and AI |Topics

## Slide 20
Datamining and AI | Project Idea
Design and implement an advanced and robust DL/ML based module that is able to predict and mitigate machine interruptions in synchrotron facilities in which should enhance users' beamtime and machine performance.
The project is real implementation of data that is collected from Synchrotron-light for Experimental Science and Applications in the Middle East (SESAME) facility.
By using such valuable data, we aim to develop a solution that anticipates potential beam instability and downtimes and also actively works to prevent them.

## Slide 21
Introduction to SESAME Facility
Introduction to the problem
Available resources
Project idea
Similar work done
Datamining and AI |Topics

## Slide 22
Datamining and AI | Literature review
Reference | Aim | Dataset(s) | Model(s) | Results
JP: A novel approach for classification and forecasting of time series in particle accelerators | Beam interruption prediction | 97 out of 376 PVs were selected through a PV evaluation method | RPCNN and RF | RPCNN model reached an AUC of 0.71 ± 0.01, outperforming the RF model's 0.65 ± 0.01 AUC.
JP: Predicting particle accelerator failures using binary classifiers,” Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment | Beam interruption prediction | The dataset includes 6987 trip-related files and 1699 notrip files, with each pulse represented as a waveform of 120000 data points | RF with techniques like FFT PCA for feature Selection. | RF distinguished normal and pre-failure conditions with precision of 0.84 and recall of 0.57 for NBL, and precision of 0.96 and recall of 0.59 for BL.
JP: Improvements of pre-emptive identification of particle accelerator failures using binary classifiers and dimensionality reduction, | To enhance previous work done “shown above” | Beam pulses from SNS, over 15 days collecting 15,000 waveforms (half good pulses and half bad pulses). | kNN, DT, RF, Gradient Boost, Logistic Regression, NN and LSVM | The Logistic Regression demonstrated the highest performance with a 79.5% accuracy in correctly identifying true negatives (bad pulses). Further refinement of datasets and tuning classifier parameters improved accuracy up to 92% for bad pulse classification.
Machine learning for time series prediction of an accelerator beam to recognize equipment malfunction | Beam interruption prediction | Acquired data from various diagnostics and MPS, including beam current waveforms before, during, and after errant beam pulses. | Employing ML techniques for anomaly detection (kNN, DT, RF, gradient boosts, LSVM, perceptrons, neural networks and logistic regression) then choosing the best to utilize LSTM autoencoders for the prediction of beam loss. | The best classifier was logistic regression with 79.5% precision for true negative prediction. When datasets were filtered and analyzed with LSTM, true negative prediction accuracy reached up to 91.9%, though the false negative rate was around 8%, which was considered too high.

## Slide 23
Datamining and AI | Literature review
Reference | Aim | Dataset(s) | Model(s) | Results
Time-series deep learning anomaly detection for particle accelerators, | Anomaly detection and fault prediction in particle accelerators, focusing on RF control system. | 670 million data points, PVs like Lock and Lock Failed statuses, Forward RF power, Tuning motor direction, moving flag, and Cryostat liquid helium tank pressure. | LSTM, TCN and Multi-variable TCN | LSTM: F-score of 0.578, precision of 0.713, and recall of 0.419. TCN: F-score of 0.642, precision of 0.743, and recall of 0.507.Multi-variable TCN: Demonstrated the best results with an F-score of 0.691, precision of 0.831, and recall of 0.516.
JP: Adaptive machine learning for robust diagnostics and control of time-varying particle accelerator components and beams | Predict dynamic changes in system components and beam characteristics. | Simulated a 22-parameter system in LANSCE linear accelerator with a potential of 1022 data points. | The approach termed AML, combines the learning capabilities of ML models like deep neural networks with the robustness of model-independent adaptive feedback control. | The model effectively tracked time-varying beam sizes in real-time, tuning input beam sizes based on end-of-beamline error measurements. It significantly minimized prediction errors compared to non-adaptive methods.
JP: Uncertainty quantification for deep learning in particle accelerator applications, | Evaluate effectiveness of BNNs in estimating predictive uncertainty in particle accelerator applications and benchmark their performance against bootstrapped neural network ensembles. | 3500 instances of beam loss rate measurements, accompanied by the settings for the 13 adjustable skew quadrupoles. 3000 for training, 250 samples each for testing and validation purposes. | BNN and bootstrapped ensembles of neural networks | BNN superior to bootstrapped ensembles in terms of prediction accuracy and uncertainty quantification, for the SPEAR3 ring, BNNs achieved an MAE of 0.055, PICP of 0.81, and MPIW of 0.19. For the LCLS beamline, the BNNs reported an MAE of 0.025, PICP of 0.75, and MPIW of 0.16. In the LCLS-II injector scenario, BNNs reached an MAE of 0.098, with PICP of 0.77 and an MPIW of 0.244,

## Slide 24
Introduction to SESAME Facility
Introduction to the problem
Available resources
Project idea
Similar work done
Possible Contributions
Datamining and AI |Topics

## Slide 25
Datamining and AI | Our contribution
All literature were done for top-up injection system, in our case bunch-by-bunch which is more challenging
Real world problem solution – real implementation
ARIMA model can be investigated in our case
RNN can be investigated ??
Sub-system based classifier --- extremely difficult
Super clear and robust data preprocessing
Making dataset available

## Slide 26
Introduction to SESAME Facility
Introduction to the problem
Available resources
Project idea
Similar work done
Possible Contributions
Challenges
Datamining and AI |Topics

## Slide 27
Datamining and AI | Problem Challenges
Dealing with huge amount of data
Finding useful data – domain experts !!
Some data might be not available or noisy
Develop a robust and reliable model otherwise it is just time wasting !!
System should be integrated with domain environment and EPICS control system.
Environment is continuously changing, is it possible to build self adapted system ??
Stand – alone system, zero end-user action.

## Slide 28
Introduction to SESAME Facility
Introduction to the problem
Available resources
Project idea
Similar work done
Possible Contributions
Challenges
System architecture and progress description
Datamining and AI |Topics

## Slide 29
Datamining and AI | System Architecture
Project Phases:
  Approval (University & SESAME)
  Reading Literature
  Domain understanding
  Field expert inputs
  Data extraction
  Data transformation & preprocessing
  ML/DL model building
  Evaluation
  Deployment
  Documentation/paper writing (going aligned with steps mentioned above)

## Slide 30
Datamining and AI | System Architecture | Data extraction & validation
Trip events:
  450 trip events for the period from March 2020 to December 2023
  Trips can be caused by any / many sub-system
  Trips recorded across different operation modes
Data Extraction & validation: events analysis -> exclude not relevant events -> exclude unrelated events -> events auto validation -> Data Availability

## Slide 31
Excluding unwanted trip events (not relevant):
  Machine time
  Power grid issues
Data Extraction & validation: events analysis -> exclude not relevant events -> exclude unrelated events -> events auto validation -> Data Availability
Machine Time:
  Testing new instruments
  Testing software / firmware
  HW/SW upgrade
Datamining and AI | System Architecture | Data extraction & validation
This affects (T)

## Slide 32
Excluding unrelated trip events:
  AUX gun
  Microtron
  Booster
  All sub-systems related to the above points
Data Extraction & validation: events analysis -> exclude not relevant events -> exclude unrelated events -> events auto validation -> Data Availability
Remember:
  3 accelerators Microtron, Booster Ring and Storage Ring.
  User beam is only available in Storage Ring (SR).
  Beam is kept there long time
  Many problems could happen in the other accelerators but not interrupting the beam in SR
Datamining and AI | System Architecture | Data extraction & validation
This affects (T)

## Slide 33
Events validation:
  A module that validates operator inputs with data recorded at EPICS archiver
Event time: Sep 18, 2023 06:19 as recorded by the operator
Exact time is Sep 18, 2023 06:21
Datamining and AI | System Architecture | Data extraction & validation
Data Extraction & validation: events analysis -> exclude not relevant events -> exclude unrelated events -> events auto validation -> Data Availability

## Slide 34
Datamining and AI | System Architecture | Data extraction & validation
Events validation:
  File output sample
Data Extraction & validation: events analysis -> exclude not relevant events -> exclude unrelated events -> events auto validation -> Data Availability

## Slide 35
Data Extraction & validation: events analysis -> exclude not relevant events -> exclude unrelated events -> events auto validation -> Data Availability
Datamining and AI | System Architecture | Data extraction & validation
Data Availability
  Year 2020 was not available STS nor LTS of archiver. We have to import them from tapes
  No data found in archiver during some trip events -- due to archiver service unavailability, maybe disk failure such records have been removed from the considerations
    2022-07-17 06:25:00
    2022-10-03 06:15:00
    2022-10-30 16:40:00
    2022-10-30 17:12:00
    2022-10-31 04:44:00
    2022-10-31 10:04:00
    2022-10-31 11:00:00
    2022-12-05 06:56:00
  The problems above affect (T)

## Slide 36
Data Extraction & validation: events analysis -> exclude not relevant events -> exclude unrelated events -> events auto validation -> Data Availability
Datamining and AI | System Architecture | Data extraction & validation
Trip data enrichment
  Some data sets were added manually
  These datasets were not recorded as trip events
  This positively affects (T)
No trip events:
  We can collect as much as we need.
  This positively affects (T)
PVs that have been added recently (i.e. in year 2023 only!!)
  SRC16-DI-PNHL:getVsize
  SRC16-CO-PNHL-THC1:getTemp
  SR-DI:getCoupling
  I11FE-CO-PHST-THC:GetTemp
  I11FE-CO-PSH-THC:GetTemp
  This negatively affects (Is)

## Slide 37
Data Preprocessing: Sliding window -> Scanned vs monitored PV
Datamining and AI | System Architecture | Data Preprocessing
Data will be collected in a sliding time window bases
TS | PV1 | PV2 | PV3 | PV4 | PVn
TS1 | V1,1 | V1,2 |  | V1,4 | 
TS2 | V2,1 |  | V2,3 | V2,4 | 
TS3 | V3,1 |  |  | V3,4 | 
TS4 | V4,1 | V4,2 |  | V4,4 | 
TS5 | V5,1 |  | V5,3 | V5,4 | 
TSj | Vj,1 | Vj,2 |  | Vj,4 | 
 |  |  |  | Vj+1,4 | 
 |  |  |  | Vj+2,4 | 
 |  |  |  | Vj+3,4 | 
 |  |  |  | Vj+4,4 | 
 |  |  |  | Vj+5,4 | 
 |  |  |  | Vj+i,4 | 
Data is imbalanced by it is nature… why ??

## Slide 38
Scanned PV @ 8 Hz
Scanned PV @ 6 Hz
Scanned PV @ 1 Hz
Monitored 100 Hz at most
Monitored 500 Hz at most
PV1
PV2
PV3
PV4
PV5
Wi
Datamining and AI | System Architecture | Data Preprocessing
Scanned vs monitored PVs
Wi-1
Sliding Size (S)
Data Preprocessing: Sliding window -> Scanned vs monitored PV
How to balance the data ?

## Slide 39
MFP | Data extracting and preprocessing
TS1
V1
Data balancing – proposed method
  Data expansion
Target PV ref.
TS2
V2
TS3
V3
TS4
V4
TSj
Vj
TS2
V1
TS5
V2
TSj
V3
Desired PV
Desired balanced PV
TS1
A1
TS2
V1
TS3
A2
TS4
A2
TSj
A
TS5
V2
A = avg (successful values with time stamps)
A2 = avg (V1, V2)
A
A
A

## Slide 40
MFP | Data extracting and preprocessing
TS1
V1
Data balancing – proposed method
  Data reduction
Target PV ref.
TS2
V2
TS3
V3
TS4
V4
TSj
Vj
Desired PV
Desired balanced PV
TS1
TS2
V1
TS3
A2
TS4
A2
TSj
A
TS5
V2
A = avg (successful values with time stamps)
A2 = avg (V1, V2)
A
A
A
TS1
V1
TS1.1
V2
TS1.2
V3
TS1.3
V4
TSj
Vj
TS1.4
V5
TS1.5
V6
TS1.6
V7
V1
TS2
V8

## Slide 41
MFP | Data extracting and preprocessing
PVs sampling rate
  Archiver vs SCAN

## Slide 42
MFP | Data extracting and preprocessing

## Slide 43
MFP | Data extracting and preprocessing
Collecting No Trip data
  Schedule
  Simi random
  # of trip events in each year / 4 quarters
  In each quarter we select randomly

## Slide 44
Thanks
Thanks
Mustafa Alzubi